## Slide 1: CWMS LOWER SNAKE ESP Development
Walla Walla District
Developed by:
  Jon Roberts, PE
  Ross Wickham, PE

## Slide 2: Overview
Lower Snake watershed and points of emphasis
CWMS goals
Vision for the ESP ensemble compute
Initial workflow priorities, timeline, and work completed
Real-time results
Next steps
Future improvements & partnership
Questions

## Slide 3: CWMS Lower Snake Watershed
Lower Snake
8 Reservoirs
35,049sq miles
5 Major consequence locations
3 Significant levee systems
River Miles Modeled:
  Snake River: 237mi
  Clearwater River: 45.5mi

## Slide 4: CWMS Goals for Lower Snake
Incorporate/Expand upon the CWMS Clearwater model
Provide WM a model that had reservoir operations capable of handling water temperature and momentum wave action once software was ready
Provide a more diverse time range for operations
  Current District CWMS uses 10-day gridded QPF
  Upgrade CWMS Clearwater model to incorporate 10d-RFC feeds
  Only really useful in 2 timeframes of the WY
      Rain-on-Snow events
      Final Fill events

## Slide 5: Vision for the ESP Ensemble
Utilizing RFC 120-day STP run, as a risk base analysis for runoff
This led to the idea of re-regulating the complete ESP data record from the raw dataset
Advantages
  Relying on the RFC expertise for the hydrology but WM staff for the regulations of the projects
  Allows WM staff to identify more applicable runoff alternatives based on current runoff-volume forecast for each of the reservoirs
  Provides a risk analysis range for possible runoffs
  Allows for the overlay plot of specific analog ESP years, to view for comparisons
  Allows for the use of updated routing from current calibrated HEC-RAS model

## Slide 6: Workflow ESP Ensemble Development
Build ResSim alternative
Data from RFC forecast points
Backing out local inflows for the RFC points
Creating inflow data for critical locations without RFC points
CAVI setup
Mapping time-specific data to current CAVI forecast
Real-time testing
Weighting of WY based on volume forecast
Graphing interface

## Slide 7: ResSim: ESP Network Setup
Palouse at Hooper
LGS
LWG
Potlatch
DWR
Brownlee
Hells Canyon
Salmon at Whitebird
Imnaha
Asotin Ck
Orofino
Non-RFC Forecast Location; inflows to be computed in relation to RFC Location
RFC Forecast Location
Anatone
CCP Inflow Location
ResSim Model Reach
Reach Not Modeled
Spalding
Tucannon near Starbuck
Lapwai Ck
RFC Routing Reach
LMN
Grande Ronde at Troy
Oxbow
IHR

## Slide 8: CAVI Setup and Initial Results

## Slide 9: CAVI Forecast and ResSim Alternative

## Slide 10: CAVI Results

## Slide 11: Future Improvements and Partnership
Graphic Interface
  Weighting of ESP trace based on WY Forecast
  Highlighting of 10/90% bands
  Highlighting of specific water analog years
Partnership with NWRFC
  Improving how data is handed off
  Adding a 10-day observed period to ESP traces
  Handing regulation runs back to NWRFC for downstream control points (current proposal is at the LWG inflow point)

## Slide 12: Questions?

## Slide 13
Ice Harbor_IN
LwSnakeRv_S110
Lower Monumental_IN
LwSnakeRv_S120
Little Goose_IN
LwSnakeRv_S140_Local
Lower Granite_IN
LwSnakeRv_S150_Local
Potlatch nr Spaldng
PotlatchRv_S10
Dworshak_IN
DWR_Inflowl
Brownlee_IN
Brownlee_Inflow
Hells Canyon
Snake+Asotin
LwSnakeRv_S170
Clearwater at Orofino
LwSnakeRv_S150_Local
Non-Inflow CCP
Snake near Anatone
CCP Inflow Location
ResSim Model Reach
Reach Not Modeled
Tucannon_HW
TucannonRv_S10
Lapwai Ck near Lapwai
LwSnakeRv_S150_Local
ResSim: Standard CWMS Network Setup
Snake+Salmon
SalmonRv_R100
Snake+Imnaha
Imnaha_Rv_R10
LwSnakeRv_S190_Local
Asotin Ck
AsotinCk_S10
Snake+Grande Ronde
GrandRondeRv_R10
Snake+Clearwater
ClearWaterRv_S10_Local
Columbia+Snake
LwSnakeRv_S100
Snake+Palouse
LwSnakeRv_S130_Local
PalouseRv_R10
Snake bl McDuff Rapids
LwSnakeRv_S180_Local
Clearwater at RM 29.68
ClearWaterRv_S20
*All inflows computed by HMS
**Not all CCPs displayed
Clearwater at Spalding
LwSnakeRv_S150_Local
Oxbow

## Slide 14
IHDW1
Ice Harbor (local)
LMNW1
Lower Monumental (local)
HOPW1
Palouse at Hooper (unreg)
LGSW1
Little Goose (local)
LGDW1
Lower Granite (local)
PRII1
Potlatch below Little Potlatch
DWRI1
Dworshak (unreg)
BRNI1
Brownlee (unreg)
*BRNI1 = HCDI1 RFC flows
HCDI1
Hells Canyon (unreg)
WHBI1
Salmon at Whitebird
IMNO3
Imnaha at Imnaha
TRYO3
Grande Ronde at Troy
Asotin Ck at Asotin
USGS 13335050
ORFI1
Clearwater at Orofino
Non-RFC Forecast Location; inflows to be computed in relation to RFC Location
RFC Forecast Location
ANAW1
Snake near Anatone (local)
Inflow Equations to Properly Account for Mass Balance:
*These are total flows, produced by RFC and used as boundary conditions
BRNI1, ORFI1, DWRI1, PRII1, HOPW1
*These are routing calcs for local flows
ANAW1local = ANAW1total – HCDI1total,routed (note: HCDI1total =BRNII1total)
LGDW1local = LGDW1total – ANAW1total,routed – SPDI1total,routed -0.16*IMNO3total,routed,Asotin (Note: 0.16*IMNO3 = Asotin)
SPDI1local = SPDI1total –PRII1total,routed– 0.14PRII1total,routed,Lapwai– ORFI1total,routed – DWRI1total,routed
LGSW1local = LGSW1total - LGDW1total,routed
LMNW1local = LMNW1total – LGSW1total,routed – HOPW1total,routed – 0.15*HOPW1total,routed,Tucannon
IHRW1local = IHRW1total – LMNW1total,routed
*These are relationships of locations without ESP data to locations with ESP data
**These are also routed in the local flow calculations
Lapwai Ck near Lapwai = 0.14*PRII1
Tucannon near Starbuck = 0.15*HOPW1
Asotin Ck = 0.16*IMNO3
CCP Inflow Location
ResSim Model Reach
Reach Not Modeled
SPDI1
Clearwater at Spalding (local)
Tucannon near Starbuck
USGS 13344500
Lapwai Ck near Lapwai
USGS 13342450
ResSim: ESP Network Setup
RFC Routing Reach

## Slide 15
Ice Harbor_IN
Lower Monumental_IN
Little Goose_IN
Lower Granite_IN
Potlatch nr Spaldng
Dworshak_IN
Brownlee_IN
Hells Canyon
Snake+Asotin
Clearwater at Orofino
Non-Inflow CCP
Snake at Johnson Bar
CCP Inflow Location
ResSim Model Reach
Reach Not Modeled
Tucannon_HW
Lapwai Ck near Lapwai
ResSim: Routing Table Names
Snake+Salmon
Snake+Imnaha
Asotin Ck
Snake+Grande Ronde
Snake+Clearwater
Columbia+Snake
Snake+Palouse
Snake bl McDuff Rapids
Clearwater at RM 29.68
Clearwater at Spalding
Oxbow
snk_to_189_89
snk_to_227_66
Snake near Anatone
snk_to_186_42
snk_to_177_48
snk_to_174_04
snk_to_167_03
snk_to_165_87
snk_to_92_02
Snake RM178.27
snk_to_61_82
snk_to_69_77
snk_to_106_15
snk_to_137_56
snk_to_143_67
RM92.02
Snake+Tucannon
snk_to_58_74
nf_cw_to_0_17
cw_to_40_71
snk_to_9_34
snk_to_40_96
Clearwater+NF
Clearwater nr Peck
lap_to_0_23
cw_to_15_19
cw_to_29_93
cw_to_37_45
cw_to_0_24
cw_to_3_94
cw_to_11_84
Clearwater + Potatch
Brownlee Flows = Hells Canyon Flows (NULL routing in ESP traces)
NULL routing
Dworshak_OUT