## Slide 1: Downloading ESP Data
Connects to NWFC website and saves ESP to DSS using R script
scripts/Download_ESP_5mins.py launches
scripts/esp_download/Download_ESP.bat, which then passes the output DSS file name ( to be saved in watershed shared) to call of calls
scripts/esp_download/ESP Download.R using R (w/ dssrip package)
Configuration of RFC locations to download set in config.xlsx file in ‘download_sites’ tab
Download_ESP_5mins.py
Download_ESP.bat
ESP Download.R
set dssfile="columbia10_6hr.dss"
R script
saveLocation = commandArgs(trailingOnly=T) ["columbia10_6hr.dss“]
‘siteIDs’ strings define sites to downloaded ESP feeds, read in from config.xlsx
See rfc_esp_links.xlsm file for the urls. Note: will only download natural ESP traces
See ‘ESP_Description_Webinar_20160518.pdf’ for more info on ESP “flavors” (pg 12) and general info
Natural is the best option for ESP. Water supply is legacy. Unadjusted has no routing.
saveLocation argument

## Slide 2: Finding NWRFC IDs
Navigate to NWRFC site: https://www.nwrfc.noaa.gov/rfc/
Click on a specific location
NWRFC ID is in parentheses next to full site name (only first four characters are needed for R script)
Tool matches site IDs against csv file names in scripts/esp_download/rfc_esp_links.xlsm using regular expressions
Uses: scripts/esp_download/ESP Download.R
Example config.xlsx ‘download_sites’ tab:

## Slide 3: Route ESP Flows
Needs to be done if you want to preserve similar routing as HMS would do for flows
Get Mod Puls (or other routing) from (RAS) analysis
See documentation on how to set up configuration
CAVI runs the scripts/Flow_Modifier.py script
Flow_Modifier.py
Flow_Modifier.py Configuration (references files shared/flow_modifier and shared directories)

## Slide 4: Run ESP ResSim Alternative

## Slide 5: 4. Save ESP Data to SQLite

## Slide 6: 5. Run GUI

## Slide 7
Main ESP Tool directory
ESP Download Tool
ESP Local Flow Tool
CAVI Folders
<Base CWMS Directory>
Additional Python scripts for CAVI
jar file for SQLite script

## Slide 9: Figures for config.xlsx

## Slide 10
Forecasts with ‘forecast.db’ SQLite files
Established in webapp/global.R script via ‘metricsToCompute’ dataframe
Interpreted from catalog IDs of time series output
Established in config.xlsx under ‘fcst_tbl’ tab
Established in config.xlsx under ‘plot_config’ tab
Established in config.xlsx under ‘current_data_tbl’ tab

## Slide 11: Mod Puls Table Extract from RAS

## Slide 12: Printf formatting
Respects html formatting. For example:
“Lower Granite<br>Elevation (ft, NGVD29)” will be interpreted similar to figure on the right. Not the ‘<br>’ syntax to indicate new line

## Slide 13: Current tbl formatting
Respects ‘printf’ formatting. For example, “%.1f” indicates a floating point value with one decimal space. “%s” indicates a string.
The inclusion of “%s” to indicate the most recent date-time of available CWMS data is optional, but the floating point value is required. If specified, the “%s” must be placed after the floating point specifier.
Example inputs, and resulting ‘Current CWMS Data’ text:
With “%s” syntax:
Without “%s” syntax:

## Slide 14: Forecast Table Configuration

## Slide 15
CCP in ResSIm
Not a CCP in ResSim
RFC Forecast Location
Not an RFC Forecast Location
CCP in ResSIm
Not a CCP in ResSim
RFC Forecast Location
Not am RFC Forecast Location
Develop relationship between another ESP forecast location to estimate flows
Neglect and account for net local flow contribution downstream as difference

## Slide 16
PRII1
Potlatch below Little Potlatch
DWRI1
Dworshak
ORFI1
Clearwater at Orofino
CCP not associated with RFC Forecast Location
CCP Inflow Location and RFC Forecast Location
ResSim Model Reach
SPDI1
Clearwater at Spalding (local)
Lapwai Ck near Lapwai
USGS 13342450
ESP Example Routing
SPDI1local = SPDI1total –PRII1total,routed– 0.14*PRII1total,routed– ORFI1total,routed – DWRI1total,routed
Lapwai Ck near Lapwai

## Slide 17
HCDI1
Hells Canyon (unreg)
WHBI1
Salmon at Whitebird
IMNO3
Imnaha at Imnaha
TRYO3
Grande Ronde at Troy
RFC Forecast Location Only
ANAW1
Snake near Anatone (local
CCP Inflow Location and RFC Forecast Location
ResSim Model Reach
Reach Not Modeled in ResSim
ResSim: ESP Network Setup
No ESP Inflows for these CCPs
Snake River
ANAW1local = ANAW1total – HCDI1total,routed
CCP Inflow Location only

## Slide 18
IHDW1
Ice Harbor (local)
LMNW1
Lower Monumental (local)
HOPW1
Palouse at Hooper (unreg)
LGSW1
Little Goose (local)
LGDW1
Lower Granite (local)
PRII1
Potlatch below Little Potlatch
DWRI1
Dworshak (unreg)
BRNI1
Brownlee (unreg)
*BRNI1 = HCDI1 RFC flows
HCDI1
Hells Canyon (unreg)
WHBI1
Salmon at Whitebird
IMNO3
Imnaha at Imnaha
TRYO3
Grande Ronde at Troy
Asotin Ck at Asotin
USGS 13335050
ORFI1
Clearwater at Orofino
Non-RFC Forecast Location; inflows to be computed in relation to RFC Location
RFC Forecast Location
ANAW1
Snake near Anatone (local)
Inflow Equations to Properly Account for Mass Balance:
*These are total flows, produced by RFC and used as boundary conditions
BRNI1, ORFI1, DWRI1, PRII1, HOPW1
*These are routing calcs for local flows
ANAW1local = ANAW1total – HCDI1total,routed (note: HCDI1total =BRNII1total)
LGDW1local = LGDW1total – ANAW1total,routed – SPDI1total,routed -0.16*IMNO3total,routed,Asotin (Note: 0.16*IMNO3 = Asotin)
SPDI1local = SPDI1total –PRII1total,routed– 0.14PRII1total,routed,Lapwai– ORFI1total,routed – DWRI1total,routed
LGSW1local = LGSW1total - LGDW1total,routed
LMNW1local = LMNW1total – LGSW1total,routed – HOPW1total,routed – 0.15*HOPW1total,routed,Tucannon
IHRW1local = IHRW1total – LMNW1total,routed
*These are relationships of locations without ESP data to locations with ESP data
**These are also routed in the local flow calculations
Lapwai Ck near Lapwai = 0.14*PRII1
Tucannon near Starbuck = 0.15*HOPW1
Asotin Ck = 0.16*IMNO3
CCP Inflow Location
ResSim Model Reach
Reach Not Modeled
SPDI1
Clearwater at Spalding (local)
Tucannon near Starbuck
USGS 13344500
Lapwai Ck near Lapwai
USGS 13342450
ResSim: ESP Network Setup
RFC Routing Reach

## Slide 19: ResSim

## Slide 21
Flow Modifier csv
ResSim ESP Alternative